Precision Infrared Radiometer (PIR) data from the 1994 UV-B Spectroradiometer 
Intercomparison held at the Table Mountain Test Facility Boulder, Colorado 
September 17, October 1, 1994.

These files can be found at the NOAA/ERL/ARL/Surface Radiation
Research Branch anonymous ftp site.

ftp -->       <titan.srrb.noaa.gov>
login as     <anonymous>
password   <your email address>

The below listed files can be found in the /pub/intercomparison_94/pir
directory.

Latitude:       40.125 degrees (40, 7', 30") North
Longitude:    105.237 degrees (105, 14', 13.2") West
Elevation:     1,689 m

The files listed as PIR###.TXT, where ### refers to the Julian date, contain 
the ancillary data from the PIR's for the days that solar spectral scans were 
taken during the intercomparison.  The data in the files is in raw form as 
logged from the instrument in mV.  The calibration factors to be applied to 
the data are listed below.

The description of the data files is as follows;

Year, Julian date, HourHourMinuteMinute (GMT), PIR (serial # 29143), 
PIR (serial # 29144), PIR (serial # 29149), the next six columns are the 
respective case and dome resistances and then the next nine columns are 
the respective standard deviations of the three PIR's, 3 case, and 3 dome 
temperatures.

The calibration factors to be used with the data listed in mV are,

Convert mVolts to Volts by multiplying (1/1000)V/mV*data before applying 
the calibration factors.

PIR Serial Number        Calibration Factor (x 10E-6 V/(W/mE2))

                                                             SRRB

                                                      C1                C2 (dome)
29143                                                 3.62             2.85
29144                                                 3.65             2.65
29149                                                 3.86             2.36|

Data manipulation equations listed below:


Calculate:
                    Case temperature                    T (case) (K)
                    Dome temperature                  T (dome) (K)

T (c/d) = 10E5/(273.09+26.3198*L+0.278237*LE2+0.0196739*LE3

where            L = ln((R (c/d))/1000)   and R (c/d) is in Ohms


                      R (case)  Case Resistance (Ohms)
                      R (dome) Dome Resistance (Ohms)

IRRADIANCE;

I(W/mE2)= V/(1000*C1) +SIGMA*T(case)E4 + C2*SIGMA*
(T(case)E4-T(dome)E4)

where  
              V                              is in (mV)
              T(case or dome)        is in (K)
              C1                            is in (V/(W/mE2)
              SIGMA                    is in (W/(mE2*KE2)  Stephan-Boltzman 
constant 5.67E10-8 (W/(mE2*KE4)